## Slide 1
Mechanical field reconstruction from limited observations
Bahador Bahmani
bb2969@Columbia.edu

## Slide 2
Motivation:
Fact:
Our experimental observations are limited by the number of sensors
Reason:
Cost or manufacture restriction
Efficient Sensor Placement Optimization for Shape Deformation Sensing of Antenna Structures with Fiber Bragg Grating Strain Sensors Jinzhu Zhou
Sometime we have a good prior knowledge about underlying physical phenomena! We know the governing PDE!
We can create many many admissible solutions using numerical solver.
Hypothesis: experimental observation is a linear combination of some of those admissible solutions
Admissible solutions from PDE solver
?
Real experiment

## Slide 3
Problem statement:
Hypothesis:
Additional structure: unknown coefficient is sparse
Dictionary of solutions (or an appropriate transformation of admissible solutions)
Measurement matrix
Least square problem
Sparse recovery
LASSO

## Slide 4
We generate 1000 snapshots for one period
Toy problem 1: data generation

## Slide 5
L2 solution
Reconstruction error: 5.605518633572185e-15
L1 solution
Reconstruction error:1.0673072250676275e-06
Toy problem 1:
Constructing data:
50% of data is randomly chosen as library
library is temporally normalized: zero mean unitary standard variation
We choose test measurements from data not included in library
LASSO solution
Reconstruction error:0.002015971351983264
lamda = .01

## Slide 7
Reconstruction Error: 0.09860999176138388
Reconstruction Error: 0.16966901383199118
The minimum possible of Epsilon was 0.7
L2
L1
LASSO
lambda = 0.005
Reconstruction Error: 0.10372515231840763
Toy problem 1: noisy measurements

## Slide 8
Toy problem 2: heat transfer in heterogenous material
Fixed temperature to 1
Fixed temperature to 0
Governing equation: parabolic PDE
We solve the above problem with finite element solver

## Slide 10
2- Down sampled and crop
Toy problem 2: Data preparation
1- we binarized the solution
Computational domain has a graph structure
0-field solution from FEM
To be as close as possible to experimental
conditions!

## Slide 11
Toy problem 2: Data preparation
we record 300 snapshots from beginning to the steady state condition
250 random snapshots are used to construct the library
For reconstruction we select from those data not presented in the library
Just 2% of measurements

## Slide 13
Toy problem 2: LASSO reconstruction without noise
Ground truth
Recovered atoms
Reconstructed
Error

## Slide 14
Toy problem 2: LASSO reconstruction without noisy measurement
Ground truth
Noisy measurement
Recovered atoms
Reconstructed
Error

## Slide 15
Conclusion:
It seems sparse learning can help a lot experimental and computational area of mechanics/material modeling
We empirically show dictionary learning is a reasonable approach for flied reconstruction from
Few measurements even in noisy conditions.